## Slide 1: Predicting Air Quality in Milan
Dan Herweg
May 2019

## Slide 2: The Air Quality in Milan is over 80% predictable using ensemble models and 5 variables, 4 of which are weather Summary
Milan struggles with air quality, an important health issue. Decision makers could benefit from being able to predict the Air Quality Index on an hourly basis
Using sensor data for weather and traffic to predict the index, it has been found that the AQI is over 80% predictable, mostly using weather variables. They are:
  Atmospheric Pressure
  Wind Speed
  Temperature
  Relative Humidity
  Traffic
The random forest and bagging model were most accurate, but the bagging model presented fewer large errors and should be preferred
Data collection should continue, and the model should be retrained regularly to overcome initial weaknesses in analysis

## Slide 4: Contents
Background
  Motivation
  Methodology
Data
  Feature Construction
  Data Exploration
Model
  Train/Test Split
  Predicting AQI
  Feature Selection
  Final Model
Conclusion
Recommendation

## Slide 5
I. Background
  Motivation
  Methodology

## Slide 6: Milan has poor air quality Motivation
https://www.wantedinmilan.com/news/milan-has-second-worst-smog-in-europe-who.html
A report by the World Health Organization has placed Milan just behind Turin and just before Naples as the three European cities with the worst levels of atmospheric pollution.
Article based on WHO report using 2016 data
Background

## Slide 7: Poor air quality affects citizens’ health Motivation
https://www.epa.gov/benmap/how-benmap-ce-estimates-health-and-economic-effects-air-pollution
Fine particles can enter deep into the lungs and enter the blood stream. Health impacts from particles include:
  Premature death
  Non-fatal heart attacks
  Aggravated asthma
US Environmental Protection Agency
Background

## Slide 8
Predicting AQI could help decision makers introduce interventions that are predicted to manage air quality in real time improving citizens’ health
Background

## Slide 9
I. Background
  Motivation
  Methodology

## Slide 10: We will take sensor data from weather and traffic to predict AQI using machine learning methods, selecting on accuracy Methodology
First, data from weather stations, pollution sensors, and traffic gates will be cleaned and explored. The Air Quality Index target variable will be constructed
Next, the numerical and categorical AQI will be computed directly and by first predicting pollutants
The best features will be selected and the best model will be chosen based on accuracy in predicting the categorical AQI
Background

## Slide 11
II. Data
  Feature Construction
  Data Exploration

## Slide 12: Data had to be extracted from files generated by sensors, cleaned and merged Feature Construction
The data had three main sources
  Weather Sensors
  Traffic Gates
  Pollution Sensors (used to calculate AQI)
Sensors measuring the same data were averaged
Data
Milan Sensor Locations

## Slide 13: Missing data was an issue Feature Construction
Data
Time
Pollution
Sensors
Sensor Data Quality
White Areas = Missing Data
Some sensors only had daily data
Some sensors had random periods of missing data
Values for missing data were imputed using random forest on the type of data that had missing values

## Slide 14: Noisy data was an issue Feature Construction
Noisy time series data with potential for measurement errors was smoothed
Data

## Slide 15: Some features were constructed by grouping raw data Feature Construction
A time of day variable was constructed by grouping hours as the following:
  Morning: 5-11am
  Mid day = 11am-3pm
  Evening = 3-8pm
  Night = 8pm-5am
Data
The vehicle length categories were selected by visually inspecting the distribution to identify a “small” mode, a “medium” mode, and a “large” tail
Small
Med
Large

## Slide 16: AQI had to be calculated and then transformed to a classifier to serve as the target variables Feature Construction
The AQI numerical calculation:
Categorical classification of AQI values:
Data

## Slide 17: Air Quality Index score and class distribution Feature Construction
Data

## Slide 18
II. Data
  Feature Construction
  Data Exploration
    Univariate
    Multivariate

## Slide 19: Temperature had a normal distribution and declined into year end Data Exploration - Univariate
Data
Degrees Celsius
Degrees Celsius
Frequency

## Slide 20: Wind speed was very right skewed, with high peaks Data Exploration - Univariate
Data
m/s
m/s
Frequency

## Slide 21: Traffic had daily and weekly patterns and a distribution with multiple peaks Data Exploration - Univariate
Data
Vehicles/Hour
Vehicles/Hour
Frequency

## Slide 22: Within traffic, different vehicle types had distinct behaviors Data Exploration - Univariate
Data
Pronounced weekend troughs vs. less visible weekends
Pronounced weekend troughsvs. less visible weekends
Pronounced weekend troughs vs. less visible weekends
Right skewed distribution vs. multi-modal distribution
Freight Vehicles
People Vehicles
Vehicles/Hour
Frequency
Vehicles/Hour
Frequency

## Slide 23: Benzine, a pollutant not in the AQI calculation, looked similar to the AQI over time Data Exploration - Univariate
Data
µg/m
Frequency

## Slide 24: However Ozone, a component of the AQI, showed a different pattern Data Exploration - Univariate
Data
µg/m3
Frequency

## Slide 25
II. Data
  Feature Construction
  Data Exploration
    Univariate
    Multivariate

## Slide 26: Pollutants are very correlated except ozone Data Exploration - Multivariate
Data

## Slide 27: Pollutants are very correlated except ozone Data Exploration - Multivariate
Data
Sulfur Dioxide, µg/m
Ammonia, µg/m
Ozone, µg/m3
PM 2.5, µg/m

## Slide 28: Weather data is not very correlated except the two radiation measures Data Exploration - Multivariate
Data

## Slide 29: Weather data is not very correlated except the two radiation measures Data Exploration - Multivariate
Data

## Slide 30: Traffic data is more correlated, and all positively correlated Data Exploration - Multivariate
Data
The only variables that seem uncorrelated are “Other” and Freight Vehicles, which are correlated with each other

## Slide 31: Traffic data is more correlated, and all positively correlated Data Exploration - Multivariate
Data
The correlation of the number of Euro 5 emissions designated vehicles and the number of medium length vehicles rounds to 1!
Vehicles
Vehicles

## Slide 32
III. Model
  Train/Test Split
  Predicting AQI
  Feature Selection
  Best Model

## Slide 33: Data limitations forced tradeoffs in choosing train and test sets Train/Test Split
Model
We do not have a lot of data
The data ends in the end of December, an unrepresentative period
  Intuitively, traffic patterns are expected to be anomalous
  Technically, the target variable distribution is unbalanced
  There is a secular decrease in temperatures and not a full year of data to compare the whole cycle
Since a sequential train/test split may not be feasible at this time, a stratified sampling technique was used to split the data
  As more data is collected, this should be revisited to reduce dependence between the training and testing set, especially when using smoothed data

## Slide 34: The distributions of the classes in the train and test sets Train/Test Split
Model
AQI
Frequency
Frequency
AQI

## Slide 35: The distributions of the classes in the train and test sets Train/Test Split
Model

## Slide 36
III. Model
  Train/Test Split
  Predicting AQI
  Feature Selection
  Final Model

## Slide 37: A naïve result serves as a benchmark Predicting AQI
Guessing the average AQI gave a mean squared error of 5,070
Guessing the modal AQI class “Acceptable” yielded an accuracy of 39%
Model

## Slide 38: Regressing each variable on AQI yielded better MSE than the naïve model by construction Predicting AQI
Model
MSE
5,070
Naïve Model
3,382
Temperature SLR

## Slide 39: Single linear regressions did not improve accuracy over the naïve model Predicting AQI
Model
Accuracy
39%
39%
Naïve Model

## Slide 40: Multiple regression methods further reduced MSE vs. SLR. The best model predicted individual pollutants to compute AQI Predicting AQI
Model
MSE
3,382
Temperature SLR
2,232
MLR to predict individual pollutants

## Slide 41: Predicting individual pollutants increased accuracy to 47% Predicting AQI
Model
MSE
39%
Naïve Model
47%
MLR to predict individual pollutants
Accuracy

## Slide 42: Ensemble classification algorithms were most accurate, with bagging at 84%, gradient boosting at 80% and random forest at 76% Predicting AQI
Model
MSE
47%
MLR to predict individual pollutants
84%
Bagging Classifier
Accuracy

## Slide 43
III. Model
  Train/Test Split
  Predicting AQI
  Feature Selection
  Final Model

## Slide 44: Several methods that have been used can inform our final choice of variables Feature Selection
Embedded methods: Random Forest Feature Importance
  RF was by far the better model so this will be weighted more heavily
Penalization methods: Lasso Coefficients
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Model

## Slide 45: Random forest rates wind speed, atmospheric pressure, and temperature as the most important features Feature Selection
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Model
Global Radiation was highly correlated with Net Radiation, had the highest MSE in solo linear regression, and universally rates below Net Radiation, so we will drop it

## Slide 46: Lasso coefficients also indicate wind speed is most important Feature Selection
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Model
Weekend is surprisingly high here even though it was ranked very low in feature importance. It is also the only temporal variable. It will be included in the final analysis

## Slide 47
III. Model
  Train/Test Split
  Predicting AQI
  Feature Selection
  Final Model

## Slide 48: Using a set of 10 features only improves accuracy from 84% to 86%, but parsimony is enhanced Final Model
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Model
86%
Random Forest Classifier
Accuracy

## Slide 49: Weekend is still not considered important by the random forest model Final Model
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Model

## Slide 50: The model can halve its features to 5 with only a small decrease in accuracy Final Model
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Model
82%
Random Forest and Bagging Classifiers
Accuracy

## Slide 51: There is no great disparity in the importance of the remaining features Final Model
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Model

## Slide 52: Random forest has 82% accuracy, misses by >2 classes 1.4%, and missed by 3 classes 0.7% Final Model
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Model

## Slide 53: Bagging also has accuracy of 82%, misses by 2+ classes 2.4% of the time, but does not miss by 3 or more classes Final Model
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Model

## Slide 54
IV. Conclusion

## Slide 55: The Air Quality Index is ~ 80%predictable on an hourly basis using mostly weather variables Conclusion
Only one traffic variable was included in the final model, and it was about as important as each of the four weather variables present
Ensemble models are better at predicting air quality from weather and traffic
This does not rule out that variables like the number of hybrid vehicles and diesel particulate filters could be valuable to air quality long term
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Conclusion

## Slide 56
V. Recommendation

## Slide 57: Decision makers should use a bagging model based on a set of 5 variables to predict the AQI in Milan Recommendation
Bagging has accuracy of nearly double that of more interpretable models using linear regression, and the incidence of large errors is less than random forest
  Large overestimates of air quality might be more beneficial to avoid. A recommendation to go outside when air quality is Bad could be more harmful to health, for example
Few variables reduces data requirements and makes clear what is important to the model in the absence of interpretable estimators
The five variables are
  Atmospheric Pressure
  Wind Speed
  Temperature
  Relative Humidity
  Traffic
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Recommendation

## Slide 58: Data collection should continue, and the model should be retrained regularly to overcome initial weaknesses in analysis Recommendation
A sequential train/test set was not practical due to small amounts of data, this approach will need to be retested to see if it is robust going forward
The model will also need to be revisited with data for other seasons, since it has only considered November and December
Picture: https://www.123rf.com/photo_20237672_turtle-on-money.html
Recommendation